# Text boxes

SCALE

SCALES & BALANCES

FEATURES

- Easy to use - frant panel configuration

- 25mm LCD display, attached backlight

- Reading lock, units conversion, Tare

- Optional Remote controller Rear display

- Battery provide up to 30 hours of continuous use.

TECHNICAL DATA

External resolution… 1/6,000

Display……….…….…25mm LCD

Keyboard…….…….… 6 keys mechanical switch

Operate temp…………0℃～+40℃

ADC……………………sigma delta

ADC update.…….……≤1/10 second

Power………………….AC adapter (9V/800mA)

Rechargeable batteries

（6V/1300mAh）

Options………………Remote controller Rear

display

DIMENSIONS（mm）

# DR SERIES CRANE SCALES

Models and specifications to change without notice

SPECIFICATIONS

| Model | DR |
| --- | --- |
| Capacity | 60kg x10g | 150kg x 20g | 300kg x 50g | 600kg x 100g |
| Max. Divisions | 6,000d |
| Display | 25mm LCD display, attached backlight |
| Keypad | 5 keys |
| Power | AC adapter (9V/800mA) rechargeable batteries （6V/1300mAh） |
| Gross weight | 2.5kg |